## Slide 1
Achmad Putra Sapujagad1, Teddy Sjafrizal1 and Rino Andias Anugraha1
Author:
Telkom University1
Design Optimization Of Polynomial Flexure Hinges For Enhanced Vibration-assisted Machining

## Slide 2
Introduction
1
2
3
4
Ultrasonic Vibration-Assisted Machining (UVAM) Illustration
W = deformation (µm)
Feed direction
w

## Slide 3
Introduction
1
2
3
4
W = deformation (µm)
Feed direction
Why Ultrasonic Vibration-Assisted Machining (UVAM) ?
W = deformation (µm)
Precision results
Ultrasonic Vibration-Assisted Machining (UVAM) employs a vibrating tool that operates at frequencies exceeding 20,000 Hz, resulting in improved cutting quality.

## Slide 4
Introduction
1
2
3
4
W = deformation (µm)
Why Ultrasonic Vibration-Assisted Machining (UVAM) ?
W = deformation (µm)
(Modified, from Rachmat et al, 2017)
(Sui et al, 2017)
Without a flexure hinge, the vibration tool actuated by piezoelectric actuators has an amplitude of only about 0.001 µm
(Li et al., 2019)

## Slide 5
Introduction
1
2
3
4
Deformation in flexure hinges and its effect on surface roughness
(Dimodifikasi, dari Wang dkk., (2021), © Author)
(Diambil, dari Gao dkk (2015), © Authors)
UVAM has been shown to significantly enhance surface roughness quality compared to conventional methods.
(Gao et al, 2015)

## Slide 6
Introduction
1
2
3
4
Types of flexure hinges
(Linß dkk., 2017)
Commonly used types include semi-circular hinges, elliptical hinges, corner-filleted hinges, and polynomial hinges.
(Linß et al., 2017)

## Slide 7
Introduction
1
2
3
4
Polynomial Hinge’s structures that affects deformation
(Diambil, dari Gu dkk., (2018)
n = Orde polynomial
h= hinge thickness (mm)
l = length hinge (mm)
This study investigates the effect of polynomial hinge design parameters and optimal combination in maximizing deformation (w) and minimizing stress (σ)

## Slide 8
Introduction
1
2
3
4
Parameters | Level 1 | Level 2 | Level 3 | Level 4 | Level 5
Orde Polynomial | 2 | 3 | 4 | 8 | 16
Hinge thickness | 2 mm | 2.5 mm | 3 mm | 3.5 mm | 4 mm
Length Hinge | 5.5 mm | 6 mm | 6.5 mm | 7 mm | 7.5 mm
Frequency = 20000 Hz
Actuated force (F) = 3500 N
Software :
Ansys Workbench 2021 = Vibration Simulation
Autodesk Inventor 2023 = Modelling
Minitab 19 = Statistical Tool
Design of Experiment

## Slide 9
Introduction
1
2
3
4
Vibration Simulation
1. Modal Analysis
The aim is to determine the natural frequency of each model.
The natural frequency shown by each model does not approach or match 20,000 Hz, therefore the simulation can proceed.

## Slide 10
Introduction
1
2
3
4
Vibration Simulation
2. Explicit Dynamic
To determine the deformation and stress in each model.
Deformation calculated is directed along the negative x-axis, and the maximum stress will be considered in the analysis.

## Slide 11
Introduction
1
2
3
4
Output Modal : Natural Frequency
The frequency used is 20,000 Hz; however, the data distribution does not indicate any values close to this frequency.

## Slide 12
Introduction
1
2
3
4
Design parameters that affect deformation
and stress ?
Explicit Dynamic
Results Analysis
The data indicate that the most influential parameter is hinge thickness, based on the obtained f-values: 73.9 for deformation and 162.56 for stress.

## Slide 13
Introduction
1
2
3
4
Recap of Parameter Designs Response
to deformation and stress
Result | Parameter |  | 
Parameter | Orde polynomial (n) | Hinge thickness (t) | Hinge length (l)
Deformation (w) |  |  | 
Stress () |  |  | 
Result | Parameter |  | 
Parameter | Orde polynomial (n) | Hinge thickness (t) | Hinge length (l)
Deformation (w) |  |  | 

## Slide 14
Introduction
1
2
3
4
Grey Relational Analysis Results
Optimal design
Rank | n | h | l | D | S | D | S | D | S |  | Stress (MPa) | Deformasi (µm)
1 | 2 | 4 | 6 | 0,053 | 0,996 | 0,947 | 0,004 | 0,346 | 0,992 | 0,669 | 39,123 | 1,479
2 | 3 | 2 | 6,5 | 0,000 | 1,000 | 1,000 | 0,000 | 0,333 | 1,000 | 0,667 | 37,978 | 0,278
3 | 16 | 2 | 7,5 | 1,000 | 0,000 | 0,000 | 1,000 | 1,000 | 0,333 | 0,667 | 308,300 | 5,928
4 | 2 | 4 | 5,5 | 0,092 | 0,988 | 0,908 | 0,012 | 0,355 | 0,977 | 0,666 | 41,173 | 0,718
5 | 3 | 4 | 5,5 | 0,059 | 0,990 | 0,941 | 0,010 | 0,347 | 0,981 | 0,664 | 40,620 | 0,528
6 | 2 | 4 | 7 | 0,056 | 0,990 | 0,944 | 0,010 | 0,346 | 0,981 | 0,664 | 40,562 | 0,512
7 | 2 | 4 | 7,5 | 0,066 | 0,988 | 0,934 | 0,012 | 0,349 | 0,977 | 0,663 | 41,217 | 0,569
8 | 16 | 2,5 | 5,5 | 0,062 | 0,987 | 0,938 | 0,013 | 0,348 | 0,975 | 0,662 | 41,383 | 0,543
9 | 2 | 4 | 6,5 | 0,042 | 0,986 | 0,958 | 0,014 | 0,343 | 0,972 | 0,658 | 41,838 | 0,432
10 | 4 | 4 | 5,5 | 0,073 | 0,980 | 0,927 | 0,020 | 0,350 | 0,962 | 0,656 | 43,270 | 0,606
Rank | n | h | l |  |  |  |  |  |  |  | Stress (MPa) | Deformasi (µm)
1 | 2 | 4 | 6 | 0,053 | 0,996 | 0,947 | 0,004 | 0,346 | 0,992 | 0,669 | 39,123 | 1,479
2 | 3 | 2 | 6,5 | 0,000 | 1,000 | 1,000 | 0,000 | 0,333 | 1,000 | 0,667 | 37,978 | 0,278
3 | 16 | 2 | 7,5 | 1,000 | 0,000 | 0,000 | 1,000 | 1,000 | 0,333 | 0,667 | 308,300 | 5,928
4 | 2 | 4 | 5,5 | 0,092 | 0,988 | 0,908 | 0,012 | 0,355 | 0,977 | 0,666 | 41,173 | 0,718
5 | 3 | 4 | 5,5 | 0,059 | 0,990 | 0,941 | 0,010 | 0,347 | 0,981 | 0,664 | 40,620 | 0,528
6 | 2 | 4 | 7 | 0,056 | 0,990 | 0,944 | 0,010 | 0,346 | 0,981 | 0,664 | 40,562 | 0,512
7 | 2 | 4 | 7,5 | 0,066 | 0,988 | 0,934 | 0,012 | 0,349 | 0,977 | 0,663 | 41,217 | 0,569
8 | 16 | 2,5 | 5,5 | 0,062 | 0,987 | 0,938 | 0,013 | 0,348 | 0,975 | 0,662 | 41,383 | 0,543
9 | 2 | 4 | 6,5 | 0,042 | 0,986 | 0,958 | 0,014 | 0,343 | 0,972 | 0,658 | 41,838 | 0,432
10 | 4 | 4 | 5,5 | 0,073 | 0,980 | 0,927 | 0,020 | 0,350 | 0,962 | 0,656 | 43,270 | 0,606

## Slide 15
Introduction
1
2
3
4
Optimization Results & With vs Without Flexure Hinge
The addition of a flexure hinge results in a deformation increase that is 9 times greater compared to the condition without a flexure hinge.

## Slide 16
Introduction
1
2
3
4
Conclusion
The optimal parameter combination for maximizing deformation (w) and minimizing stress (σ) is achieved with a model featuring a polynomial order n=2, hinge thickness of 4 mm, and hinge length of 6 mm. This model results in a deformation of 1.479 µm, which is significantly greater compared to the maximum deformation of 0.161 µm observed without a flexure hinge. The resulting stress is also relatively low at 39.1 MPa
Main Contributions
This study is among the first to investigate the impact of polynomial hinges on deflection in Vibration Assisted Machining.
We successfully investigated the effect of changing the polynomial design parameters on deflection and stress using the finite element method.
We managed to demonstrate the piezoelectric character to apply on finite element analysis and loaded condition.

## Slide 17
Introduction
1
2
3
4
Thank You