## Slide 1: Vibration Diagnostic Approach Utilising Finite Element Analysis on Reciprocating Machine for Offshore Facility
By:
Mohamed Fuad Al Farabi Shazi Staff Engineer, Rotating Equipment
Presentation to ICoMSETA 2024
2 September 2024

## Slide 2: Content
5
7
6
1
3
2
4
Background
Methodologies
Event Chronology
Equipment Overview
Root Cause Analysis
Outcome & Discussion
Conclusion

## Slide 3: 1. Background
An unmanned offshore facility with 3 units of gas lift compression equipment (Unit-A, Unit-B, & Unit-C) has been operating for more than 20 years since commissioning.
Due to operational demand, changes were made on the operating philosophy with documented Management Of Change to identify potential risks or hazards with mitigated actions.
Multiple compressor failures were recorded since the change took place. Root Cause Analysis was performed and leads to the execution of advanced vibration analysis for a long-term resolution.

## Slide 4: 2. Equipment Overview
Features | Details
Construction | 2 Stage Reciprocating Compressor (2 throw)
Medium | Natural Gas
Service | Gaslift
Speed | Compressor: 375 rpm (6.25 Hz); Engine: 1110 rpm (18.5 Hz)
Philosophy | 3 X 50%
Compressor
2nd Stage Comp
Gas Engine
LP Gas
HP Gas
Inlet scrubber
2nd stg Scrubber
Cooler
Speed Reducer
Source: I (wordpress.com)

## Slide 5: 3. Event Chronology: The Timeline
Commissioning & operation
Overhaul + new piston
New operating philosophy
Restart compressor
1st piston failure
Consolidate findings
Inspection
2nd piston failure
Revised from
3 X 50% to
3 X 33.3%
Suspected liquid carryover from scrubber
Unit manually stopped due to knocking sound during walkabout surveillance
Deployed Frontline Maintenance Team
Significant floor vibration around engine area
Resonance suspected
Material debris and wreckage
Piston nut loose
Suction scrubber auto-drain malfunction
Failure observed on 1st stage

## Slide 6: 3. Event Chronology: Increase in vibration trending
Vibration exhibited on Unit-C shows increment in magnitude (taken when running all 3 compressors)

## Slide 7: 4. Root Cause Analysis
Compressor Piston Multiple Failure
Piston Half not intact
Liquid carryover from scrubber
Material and manufacturing defect
FOD into compressor
No PPM – Manual Drain
No QA/QC report for the purchased component
2 different assembly instruction by OEM
Operating close to structural natural frequency
Inadequate/over torque
on piston nut
Auto-drain malfunction
Casting process imperfection
High moisture content
Prolonged vibration – mechanical looseness and other related failures
Piston nut loose
Substandard material
Assembly failure
Changes in current gas composition
X
1
2
3
4
X

## Slide 8: 4. Root Cause Analysis
Compressor Piston Multiple Failure
Piston Half not intact
Liquid carryover from scrubber
Material & manufacturing defect
FOD into compressor
No PPM – Manual Drain
2 different assembly instruction by OEM
Operating close to structural natural frequency
Inadequate/over torque
on piston nut
Auto-drain malfunction
Casting process imperfection
High moisture content
Prolonged vibration – mechanical looseness & other related failures
Piston nut loose
Substandard material
Assembly failure
Changes in current gas composition
X
1
2
3
4
X
Experimental Modal Analysis was employed to resolve the RESONANCE issue
No QA/QC report for purchased component

## Slide 9: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
Develop
IDENTIFY
Verify
Simulate
Modify
Affirm
Resolving Resonance Issue
6 Steps To Resolve Resonance Using Modal Analysis

## Slide 10: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Structural skid Bump Test
Identify existing natural frequencies
Best performed during Turnaround
1

## Slide 11: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Model Development
FEA model was derived based on numerical calculations on a particular machine
ODS shows the motion of structure under various forces – Highest at Engine
Verification via FRF
Frequency Response Function (FRF) Modal analysis was employed to determine dynamic characteristic (Natural frequencies, mode shape, damping)
Used to establish correlation between MA and FRF
2

## Slide 12: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Verification of Resonance
Modal analysis revealed dominant horizontal mode at 19.5Hz which is very close to the engine running speed of 18.5Hz.
The overall condition was considered dynamically weak and classified as a Near Resonance issue.
Engine running frequency 18Hz – 20Hz
3

## Slide 13: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Structural Dynamic Modification (SDM)
SDM allows any modification to be performed in a virtual environment
Addition, removal, or modification of the structural geometry/assembly to shift natural frequency away from operating speed.
API 618 (7.9.4.2.5.3.2) “ The predicted mechanical natural frequencies shall be designed to be separated from significant excitation frequencies by at least 20%. ”
Figure | FEA (Original) | SDM
 | 19.4 Hz | 18.9 Hz (-2.5%)
 | 19.4 Hz | 22.5 Hz (+16%)
 | 19.4 Hz | 27.9 Hz (+44%)
 | 19.4 Hz | 23.0 Hz (+18%)
4

## Slide 14: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Selected based on the ease of implementation with the highest probability of success
Accessibility for implementation
Shutdown window availability
Evaluate Economic benefits
Identify existing obstacles and challenges prior to the modification
Execute & Considerations
5

## Slide 15: 5. Methodologies
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Sales | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333 | 0.083333
DEVELOP
IDENTIFY
VERIFY
SIMULATE
MODIFY
AFFIRM
RESOLVING RESONANCE ISSUE
Pre-Modification
Post-Modification
Original vibration level for high frequency harmonics
Significant vibration amplitude reduction on high frequency harmonics
Further improvement; i.e., verify model accuracy, install additional rubber isolators, support beam extension
6

## Slide 16: 6. Outcome & Discussions
Continuous high vibrations over a long period can cause significant damage, and in some cases lead to safety and environmental issues.
Attention to details: Ensure assumptions used in modelling is as accurate as possible to the actual machine construction.
Structure support integrity may impact the overall outcome. Remember to include reasonable tolerances in the analysis.
Original FEA model without Structural horizontal beams
Corrected model with Structural beams

## Slide 17: 7. Conclusion
2
Once the weak and flexing points are identified, appropriate stiffening options were analysed and selected to improve the overall vibration levels.
3
Successful collaboration with Mechanical, Civil & Structure, Piping, Turnaround Team, Operations, and Association with Institutional of Higher Learning to resolve complex vibration issue.
1
From the Finite Element Analysis, it was evident that structural strengthening is required due to resonance.

## Slide 18
Questions