## Slide 1: Enhancing Packing Processes through an Ergonomic Worker Study using Digital Human Modeling and Environmental Assessment
Researcher
Pratzanee Sungkaratn
Sukhothai Thammathirat Open University, Thailand

## Slide 2: Page 1 of 18
Sukhothai Thammathirat Open University, Thailand
Introduction
A manual lifting is the transporting or supporting of a load (including lifting, putting down, pushing, pulling, carrying or moving) by hands or body force

## Slide 3: Source : Thailand ministry of labour
Sukhothai Thammathirat Open University, Thailand
Introduction
Chart: 
| 1. Cut or wounded by sharp material | 2. Injured by falling object | 3. Injured by thrown object | 4. Foreign object/chemical in eye | 5. Being pressed or pulled by object | 6. Fell from a height | 7. Fell over or slipped | 8. Car accidents | 9. Burns from exposure to hot objects/materials | 10. Animal attacks | 11. Affecte by toxic substances or chemicals | 12. Injury from lifting heavy object | 13. Electric shock | 14. Injured/burned by exposure to light | 15. Repetitive motion injjury | 16. Injured by explosion | 17. Other physical injuries | 18. Injury from fallen building | 19. Injured/burned by radiation | 20. Frostbite
 | 17415 | 12522 | 10607 | 8447 | 6806 | 5903 | 4261 | 2509 | 1572 | 1092 | 818 | 763 | 726 | 457 | 404 | 361 | 126 | 29 | 9 | 5
 | 0.22771 | 0.39145 | 0.53014 | 0.64059 | 0.72958 | 0.80677 | 0.86248 | 0.89529 | 0.91585 | 0.93012 | 0.94082 | 0.9508 | 0.96029 | 0.96626 | 0.97155 | 0.97627 | 0.97792 | 0.97829 | 0.97841 | 0.97848
Injury from lifting heavy object 763 cases.
No death, 1 invalidity, 1 lose some organ, 761 off work
Repetitive motion injury
THAILAND OCCUPATIONAL INJURIES CLASSIFIED BY CAUSE 2022
Page 2 of 18

## Slide 4
Sukhothai Thammathirat Open University, Thailand
Maximum weight allowance
Introduction
Country / Organization | Gender / Age | Allowance Weight
Thai Labor laws | Female over 18 years old Male over 18 years old | 25 kilograms 55 kilograms
Japan | For Female | 30 kilograms for non-continuous lifting 20 kilograms for continuous lifting.
Philippines | No mention gender | no more than 55 kilograms and the lifted weight should not exceed 40% of the worker's body weight
Australia | Female over 18 years old | 16 kilograms.
International Safety Data Center | Female 18-20 years old Female 20-35 years old Female 35-50 years old Female over 50 years old | 14 kilograms 15 kilograms 13 kilograms 10 kilograms
Page 3 of 18
Source : The National Labour Research Center

## Slide 5: Page 4 of 18
Purpose of the study
Sukhothai Thammathirat Open University, Thailand
The aim of this study is to improve the lifting process for 25kilogram boxes vertically stacked on pallets by maximum allowance, with consideration for the inclusion of female workers as per Thai labor regulations. Utilizing the National Institute for Occupational Safety and Health (NIOSH), Composite Lifting Index (CLI) through Digital Human Modeling (DHM) and the risk of musculoskeletal disorders (MSDs) from a single worker lifting who performs 6 lifts per hour and works 8 hours a day.
Propose
Purpose of the study

## Slide 6
Sukhothai Thammathirat Open University, Thailand
Study Questions
1. How much NIOSH recommended weight for the study process?
2. How risk of MSDs levels by NIOSH Lifting Index ?
3. How to enhance the process while maintaining safety?
Propose
Page 5 of 18

## Slide 7: \
Sukhothai Thammathirat Open University, Thailand
Recommended Weight Limit
NIOSH91 :
Where: RWL = Recommended Weight Limit
LC = Load Constant 23 kgs.
HM for Horizontal multiplier, equal 1.0 if hand location is less than 250mm
VM for Vertical multiplier, the absolute value from optimum height 750mm
DM for Distance multiplier, is the travel distance of hands that computed
AM for Asymmetric multiplier, equal 1.0 when lifted directly in front of body
FM for Frequency multiplier, is defined by frequency of lifting
Methodology
Page 6 of 18

## Slide 8
Sukhothai Thammathirat Open University, Thailand
Lifting Index (LI)
The goal of ergonomic risk assessment in designing manual lifting tasks is to achieve an LI of 1.0 or less as NIOSH Criteria for Risk Levels of Lifting Index (LI)
Lifting index | Criteria
LI <1 | Safe, low risk.
1 ≤ LI < 3 | Moderate risk; consider ergonomic improvements.
LI ≥3 | High risk: immediate ergonomic intervention needed.
Methodology
LI is calculated using the following equation:
Page 7 of 18

## Slide 9
Sukhothai Thammathirat Open University, Thailand
Research methodology
To assess and improve the process, evaluating the Lifting Index is crucial for risk assessment using Tecnomatix software calculations.
The default tasks in a packing room were observed to create DHM.
Methodology
Worker shortest height in the process 148 cm
Page 8 of 18

## Slide 10: Page 9 of 18
Sukhothai Thammathirat Open University, Thailand
TECNOMATIX NIOSH simulation report
Methodology
CLI
RWL
LI
6 lifts per hour

## Slide 11
Sukhothai Thammathirat Open University, Thailand
Composite Lifting Index (CLI)
Since this study is multi-task lifting, The Composite Lifting Index has been
considered two identical boxes as equation
Where STLI is computed for Single Task Lifting Index for each task
Methodology
Page 1 0of 18

## Slide 12: Page 1 1of 18
Sukhothai Thammathirat Open University, Thailand
Design process option
Then design improvement processes for three options
1. assigning tasks to two workers for manual lifting without assistive tools
2. implements a system where height adjustment precedes solo lifting
3. utilizes a spring balancer to aid in lifting the box.
Methodology

## Slide 13: Page 1 2of 18
Chart: Model of workers height
| male1 | male2 | male3 | male4 | female1 | female2 | female3 | female4
model | 1543 | 1583 | 1678 | 1775 | 1449 | 1484 | 1570 | 1659
Sukhothai Thammathirat Open University, Thailand
Simulation flow
Methodology
Set position Box1
Set position Box2
Run Simulation
Get NIOSH LI report
Set up Load
Set lift frequency
Create models
START
Finish all models?
No
New process design?
Yes
Yes
No
End

## Slide 14: Photo of simulation for model female height at 5th percentile stacked 2nd box vertically at the hand position4 height 1180millimeters
Sukhothai Thammathirat Open University, Thailand
Height and Hand positions results
Result
Page 13 of 18

## Slide 15
Sukhothai Thammathirat Open University, Thailand
Composite Lifting index results
Result
The default process, one worker.
maximum CLI is 3.93
Option 1. two workers lifting,
Max resulted in a CLI of 1.97
Option 2. height adjustment, one worker. Max resulted in a CLI of 2.77
Option 3. utilizes a spring balancer,
load reduce to 3 kg and boost lift frequency to 1 lift/min. (10 times)
Max resulted in a CLI of 0.47
Page 14 of 18

## Slide 16: Page 1 5of 18
Sukhothai Thammathirat Open University, Thailand
Compare CLI and carbon emission
Result
The default process requires operators to work 8 hours a day to transport 40 boxes. (6 lifts per hour)
From the factory indicates an annual electricity consumption of 18,900 kWh. The factor used is 0.5610 equal to 10.6tCO2e per year.
The option 3 which CLI is 0.47 boosted to the highest efficiency (60 lifts per hour), the tasks can complete within 0.72 hours a day, resulting in the lowest electrical consumption equal 0.96tCO2e per year.

## Slide 17
Sukhothai Thammathirat Open University, Thailand
Conclusion
The risk of MSDs from the packing process is high when handling vertically stacked 25-kilogram boxes on pallets. The recommended weight only 6.36kgs. by work an 8-hour day, as NIOSH CLI equation.
This study recommends simply and effective engineering improvement the process by spring balancer assistance. Then productivity can safely increase 10x. thereby reducing cycle times, number of required workers and the carbon emissions.
There are more improvement by human management or robust process design which have not discussed in this topic.
Discussion
Page 1 6of 18

## Slide 18
Sukhothai Thammathirat Open University, Thailand
We request you to provide the suggestion.
Thank you.
End
Page 18 of 18